If the Soil Factor Mix used in Toyo-Mulching® System is poisonous?

## By Hinson Lau

Toyo-Mulching System (TMS) is being regarded as a magical breakthrough in the landscaping industry as it makes  vegetation growing healthily on the concrete slope surfaces.  It not only stabilizes slope of whatever natures but also create a naturally green living environment. The Soil Factor Mix being adopted in TMS is the core soft component that contributes to the success of TMS.  However, what are the ingredients of the Mix and does it contain any harmful materials?

WHAT IS TOYO-MULCHING SYSTEM?

Being the most advanced vegetation technology in Japan, Toyo-Mulching System (TMS) was introduced into Hong Kong in 1998. Because of its ease to use feature and reliable output quality, this method is widely adopted in Japan and Taiwan for more than 20 years.

The principle of TMS is to establish a self-sustained vegetation ecology, which will continuously provide necessary nutrient and water to the vegetation itself.  This method can be applied on any non-soil surface such as bedrock, sprayed concrete, mortar, no-fine concrete or chunam.

The TMS includes permanent hard and soft components.

### INPUT

PROCESS

OUTPUT

TMS is a mature

technology which

can be customized

to fit different landscape

environments and

vegetation requirements.

The Soil Factor Mix is the soul of the new vegetation. So, what does it consist?  Is there any material that is harmful to the plants or even human beings?

WHAT’S THE INGREDIENTS OF THE SOIL FACTOR MIX?

Soil Factor Mix is the main planting media of TMS.  It is a proprietary product supplied by Nisshoku Corporation in Japan. This mixture not only provides nutrient but also moisture necessary for the establishment of vegetation.  This Soft Factor Mix has high gas permeability, water-retaining capacity and can retain the fertilizer for a long period of time.  Basically, the Soil Factor Mix consists of 2 main categories of materials:  effective bonding agents and long lasting fertilizers.  Its detail ingredients as follows:-

- long lasting aldelyde process resin form fertilizer

- water soluble fertilizer

- water retaining polymer

- organic moisture retaining agent

- composed organic fertilizer

- resin form bonding agent

- germination stimulator

Bonding agent - Basesoiler is the main bonding agent in the Soil Factor Mix. According to the Nissshoku’s laboratory evaluation, it is proved to be an effective material that can minimize the washout as well as control surface erosion. Thus, the Soil Factor Mix can stick onto rock mass or other non-soil slope surface firmly and prevent the mixture from eroding and being broken by rain or any other natural factors.

Long lasting fertilizer - With the long lasting aldelyde process resin form fertilizer, the Toyo-Mulching System can establish a self-equilibrium vegetation ecology that will continuously provide the necessary nutrient and moisture for the vegetation.

ANY ALDEHYDE RESIN IN SOIL FACTOR MIX?

Currently, there is a public query that if  TMS is really contributive in building a “safe”  slope? If the Soil Factor Mix contains aldehyde resin? To ease the public concern, it has been verified by the supplier Nisshoku Corporation in Japan that the Soil Factor Mix does not contain any aldehyde resin nor does it release hazardous fume when it catches fire.  In TMS, the term aldehyde resin is just being deployed as an adjective to describe the chemical process in manufacturing the long lasting fertilizer. The term Aldehyde is a class of organic compounds that are commonly used in manufacture plastic and dyes. Resin is the organic substance from plants. As described in the Encyclopedia dictionary, it is a solid or semisolid natural organic substances secreted in the sap of some plants and trees that has a transparent or translucent quality and a yellow or brown color.  Anyhow, the Soil Factor Mix does not include any harmful materials.

Figure.1 Spraying of Soil Factor Mix

# Text boxes

##### Toyo-Mulching System

Hard Component : permanent high strength PVC coated galvanized iron mesh

Soft Component : unique Soil Factor Mix consisting fertilizer, soil bonding agent, water retaining agent & vegetation

Growth of self-substained & healthy vegetation

( safe and environmental harmony living environment

Types of TMS:

- General TMS

- Strip TMS

- Creat TMS